## Slide 1
New HTS projects in Europe
Mathias Noe, KIT
30.01.2017, Milano, Italy
IEA ExCo Meeting

## Slide 2: Cost effective FCL using advanced supercon. tapes for future HVDC grids
Significant advances of the economical attractiveness of SCFCL by improving the REBCO tapes especially in their normal mode.
Advanced REBCO tape
  Low standard deviation in term of Ic on the lengths
  Electric field higher than 100 V/m (50 ms)
  Critical current higher than 1000 A/cm-w at 65 K (self field)
Emerging REBCO tape
  Enhanced propagation velocity tape (CFD concept)
  Sapphire substrate REBCO tape with ultra high electric fields
Smart module of a HVDC apparatus
  Current and voltage in the range of 0.5/1 kA and 30/50 kV
  New functionality such as quench detection through fiber glass
  Extensive tests of this module in relevant environment
H2020 project
42 months
Starting: 01/2017
Coor.: CNRS

## Slide 3: ASuMED Advanced Superconducting Motor Experimental Demonstrator
Participants
OSWALD Elektromotoren GmbH, Germany
ROLLS-ROYCE PLC, United Kingdom
UNIVERSITY OF CAMBRIDGE, United Kingdom
KARLSRUHER INSTITUT FUER TECHNOLOGIE, Germany
HOCHSCHULE FUR ANGEWANDTE WISSENSCHAFTEN ASCHAFFENBURG, Germany
AIR LIQUIDE ADVANCED TECHNOLOGIES SA, France
DeMaCo Holland bv, Netherlands
SuperOx, Russian Federation
Institute of Electrical Engineering, Slovak Academy of Sciences, Slovakia
K & S GMBH PROJEKTMANAGEMENT, Germany

## Slide 4: Background & Motivation
Air traffic projected to grow worldwide by 5% per year  increasing fossil fuel consumption and emissions
Previous studies: hybrid-electric distributed propulsion (DP) in civilian aircraft offers a route to achieve massive reductions in fuel consumption and emission (targeted by Flightpath 2050)
Studies identify necessity of potential superconducting solutions to achieve required power densities and efficiencies
However, no suitable superconductive motor is available to realize DP in large aircraft and no prototypes have been constructed with this aim

## Slide 5: Purpose
Demonstrate benefits of a new fully superconducting motor with a power density of 20kW/kg. In particular:
  design an appropriate motor topology
  develop a high-temperature superconducting (HTS) stator with an electric loading of >450kA/m
  develop a rotor using HTS stacks operating like permanent magnets providing an average magnetic loading of >2.5 T
  integrate a magnetization system into the stator area
  implement a highly efficient cryostat for motor combined with integrated cryogenic cooling system and associated power converter
Demonstrate above technologies in a prototype with approximately 1 MW power at 10.000rpm and a thermal loss <0.1%
Design innovative modular inverter topology with enhanced failure protection, to realize highly dynamic and robust control of superconducting machines.